How to flash the binaries of the ESP32 edition of TCode controller

Extract the zip archive.
(Linux/Mac users click here viewing the the batch content should be simple enough to extract the command needed)

(Windows users)
Run “flash.bat”
Enter the COM port your ESP32 is on. Example: COM12

You should see something like this in the terminal

Now that your image is flashed time to configure the wifi if you wish to do so
IMPORTANT! The ESP32 we are using currently is ONLY compatible with 2.4ghz WiFi

You can either configure with the Android app or via the AP mode instructions below.

Reboot the ESP32
Check your available wifi networks

Connect to TcodeESP32Setup (leave connect automatically unchecked)
No password
Once connected (It can be slow be patient. About 30 secs or so)

Open your internet browser and navigate to 192.168.1.1

Enter your wifi ssid and password and change the network info if required

And wait for the Settings saved text to appear..

Click restart device or unplug and re-plug the usb powering the ESP32.

Your device should reboot and connect to the network.

You can verify this by using serial monitor

Or by logging into your router and looking for A Device named “TcodeESP32”
You should now be able to access the configuration page from or what ever you type into the Host name field on the configuration.

Once you have this IP address you can get into your machine settings via the web browser.

From here you can view the default pin out and change them if you know what you are doing.

You can also set the default servo zeros.
If you are using this in an OSR MAKE SURE YOU UNCHECK “SR6 Mode”

Enjoy your wireless device!

PS.. this release is in its early stages with missing features and bugs. if you find any issues please report them on Github.